## Slide 1
Smartphone Camera Technology
A training guide for product & marketing teams
01

## Slide 2
SECTION
Module 1: Camera Fundamentals

## Slide 3
What is a Camera Module?
A complete optical system packed into millimeters
Contains sensor, lens, autofocus, OIS, and IR filter
Five stacked layers from lens to circuit board
Each layer adds capability but also Z-height cost
03

## Slide 4
The Five-Layer Stack
Lens assembly — focuses light onto the sensor
IRCF (IR cut filter) — blocks infrared light for accurate color
CMOS sensor — converts photons into electrical signals
VCM actuator — drives autofocus movement
Flex PCB — carries data and power to the main board
04

## Slide 5
Key Sensor Specs
Pixel size: larger pixels capture more light
Optical format: bigger sensor = better low-light but more space
Resolution: megapixels matter less than pixel quality
BSI vs stacked architecture trade-offs
05

## Slide 6
Autofocus Technologies
Technology Speed Cost Thickness
─────────────────────────────────────
PDAF Fast Low Thin
Laser ToF Medium High Moderate
DW-PDAF Fastest High Thin
06

## Slide 7
SECTION
Module 2: Physical Constraints

## Slide 8
The Z-Height Problem
Every millimeter of thickness is a design battle
OIS mechanism alone adds ~0.3 mm
Larger sensors require longer focal length
Periscope design folds the optics sideways
08

## Slide 9
OIS vs Thinness Trade-off
OIS requires mechanical float — uses space
Without OIS, night shots blur from hand movement
Sensor-shift OIS moves sensor, not lens
Decision depends on target use case and price tier
09

## Slide 10
Periscope Architecture
Prism bends light 90° inside the module
Achieves 5–10× optical zoom in a thin body
XY footprint trades off against Z savings
Flagship phones only — high cost and complexity
10

## Slide 11
SECTION
Module 3: Multi-Camera Systems

## Slide 12
Why Multiple Cameras?
Single lens can't do wide + zoom + portrait simultaneously
Each focal length needs its own optical system
Software stitches views during capture and zoom transitions
ISP coordinates exposure across all sensors in real time
12

## Slide 13
Camera Roles in a Typical Flagship
Ultra-wide (13–16 mm): architecture, landscapes, selfies
Main (24–28 mm): everyday shooting, best IQ
Periscope tele (65–120 mm): portraits, reach, compression
13

## Slide 14
Thank You
Questions? Reach out to the product team.
14